Here is a comparison table between SIGLENT Spectrum Analyzers (SSA) and SIGLENT Spectrum Vector Network Analyzer (SVA) models.

| Model Specifications | SSA3000X Series | SSA3000X Plus Series | SVA1000X Series |
| --- | --- | --- | --- |
|  | SSA3021X | SSA3032X | SSA3021X Plus | SSA3032X Plus | SVA1015X | SVA1032X |
| TG | Standard | Standard | Standard |
| SA Bandwidth | from 9 kHz to 2.1 GHz | from 9 kHz to 3.2 GHz | from 9 kHz to 2.1 GHz | from 9 kHz to 3.2 GHz | from 9 kHz to 1.5 GHz | from 9 kHz to 3.2 GHz |
| VNA Bandwidth | - | - | from 10 MHz to 1.5 GHz | from 100 kHz to 3.2 GHz |
| VNA Calibration Kit | - | - | F503ME |
| DANL | -151 dBm (RBW 10Hz) -161 dBm, Normalized to 1 Hz | -161 dBm/Hz | -156 dBm/Hz | -161 dBm/Hz |
| RBW | from 10 Hz to 1 MHz (1Hz setable) | from 1 Hz to 1 MHz | from 1 Hz to 1 MHz |
| Phase Noise | < -98 dBc/Hz@1 GHz, 10 kHz offset | < -98 dBc/Hz@1 GHz, 10 kHz offset | < -98 dBc/Hz@1 GHz, 10 kHz offset |
| Options | AMK/EMI/Refl | AMK/EMI/AMA/DMA | AMK/EMI/AMA/DMA/DTF |
| AMK | CHP/ACPR/TOI/OBW/Monitor | CHP/ACPR/TOI/OBW/Monitor/Harmonic/CNR | CHP/ACPR/TOI/OBW/Monitor/Harmonic/CNR |
| AMA | - | AM/FM | AM/FM |
| DMA | - | ASK/FSK/PSK/QAM | ASK/FSK/PSK/QAM |
| EMI filter | 200 Hz, 9 kHz, 120 kHz | 200 Hz, 9 kHz, 120 kHz, 1MHz | 200 Hz, 9 kHz, 120 kHz, 1MHz |
| Touch Screen | - | Touch Screen, Mouse and Keyboard, Webserver | Touch Screen, Mouse and Keyboard, Webserver |